## Slide 1: Code overview

## Slide 2
@IterativeOptimization
@SeqOptimization
@SeqJacobian
@SPGR_Jacobian
@SPGR_Tissue
@TissueParams
@SPGR_Protocol
@SeqProtocol
@???_Tissue
e.g. Yarnykh
@???_Protocol
e.g. Yarnykh
@???_Jacobian
e.g. Yarnykh
@???Optimization
e.g. SimulateAnnealsing

## Slide 3
@SPGR_Tissue
@TissueParams
Public Properties | Public Methods
None | save(obj, fileName) load(obj, fileName) paramsArray = getParams(tissueKeys) paramValue = getParameter(paramKey)
Public Properties | Public Methods
paramsKeys = {'F', 'kf', 'R1f', 'R1r', 'T2f', 'T2r'} fitParamsKeys = {'F', 'kf', 'R1f', 'T2f', 'T2r'} | SPGR_Tissue(paramsValues) paramsValues: Array of values for paramsKeys

## Slide 4
@SPGR_Protocol
@SeqProtocol
Public Properties | Public Methods
None | save(obj, fileName) load(obj, fileName) prot = getProtocol() **Abstract** totalNumOfMeas = getNumberOfMeas() paramValue = getParameter(protKey) remove(indices)
Public Properties | Public Methods
fitProtKeys = {'B1_IR', 'B1_VFA'} B1_value = 1.0 | SPGR_Protocol(fileName) fileName: qMRLab saved protocol *.mat string totalNumOfMeas = getNumberOfMeas() paramValue = getParameter(protKey) remove(indices)

## Slide 5
@SPGR_Protocol
@SeqJacobian
Public Properties | Public Methods
None | SeqJacobian(@SeqProtocol, @TissueParams) jacobianMatrix = getJacobian() *jacobianStruct = getJacobianStruct() computeOpts = compute(computeOpts) computOpts: Struct with the following properties: mode: 'New', 'Resume', or 'Completed' paramsOfInterest: Cell array of strings of fitParamsKeys to calculate Jacobian. lineBuffer:
Public Properties | Public Methods
None | SPGR_Jacobian(@SPGR_Protocol, @SPGR_Tissue)
*jacobianStruct properties:
jacobianMatrix
paramsKeys
paramsVals
protocol
status
completedLines
signal
d_signal

## Slide 6
@IterativeOptimization
@SeqOptimization
Public Properties | Public Methods
None | *Static* paramError = minimizeParamErrorBecauseOfMeasError(paramJacMat, measJacMat, measError) fisherInformationMatrix = calcFIM(jacobianMatrix) crlb = calcCRLB(jacobianMatrix)
Public Properties | Public Methods
metricSet = {'CRLB'}; | IterativeOptimization(@SeqJacobian, opts) opts: Struct with the following properties: fitParams: Cell array of strings of fitParamsKeys to include in optimization (cols of Jac.) (optional) b1Params: Cell string of B1 params name for B1-sensitivity optimization) computeSingle(metricFlag) computeDoubleAlternate(metricFlags) computeRegularized(metricFlags, regularizationCoeff) rankedAcqPoints = getRankedAcqPoints() metricValsAcqPoints = getMetricValsAcqPoints() reguTermValsAcqPoints = getReguTermValsAcqPoints() [rankedAcqPoints_sorted, metricValsAcqPoints_sorted] = getSorted() [rankedAcqPoints_sorted, reguTermValsAcqPoints_sorted] = getSortedRegTerm() [rankedAcqPoints_sorted, protocol_sorted] = getSortedProtocol()

## Slide 7: Theory Overview

## Slide 8: MRM Paper theory

## Slide 9: Updated approach
Solve min for given

## Slide 10
MRM Paper
Current Work
Parameter fitting error in simulations
: min

## Slide 11: for uniform protocols /w varying FA and #offsets?

## Slide 12: WM tissue parameter values
F = 0.15 n.u.
kf = 4.0 s-1
T1,f = 900 ms
R1,r = 1 s
T2,f = 30 ms
T2,r = 12 𝝁s

## Slide 13: Protocol definitions
Single FA
  150
  400
  650
2FA
  (150, 400)
  (150, 650)
  (400, 650)
3FA
  (150, 400, 650)
Offset values
  [300 Hz, 20 kHz]
  uniform-logarithmically spaced
  Total # of points ranging from 8 to 30
    Single FA, 8:2:30 offsets
    2FA, 4:1:15 offsets
    3FA, 3:1:10 FA

## Slide 14: Protocol pre-procesing
Calculate higher « protocol resolution » Sf cache, then set-up each protocol using that Sf cache.
Some protocol points (<5%) produced erroneous/outlier (non-continuous) Jacobian element values
  Form further testing, likely due to poor interpolation.
Identified all such point in the higher « protocol resolution » set, and if an outlier point was present in a studied protocol, change it to the nearest neighbour from high res.

## Slide 21
instead?

## Slide 22: Jacobian/Sensitivity plots

## Slide 27: Iterative CRLB Optimization
Cercignani’s Fisher Information/Cramer-Rao Lower Bound equations
, considering all n-1 protocol combinations

## Slide 28: Iterative CRLB Optimization; comparison with Ives

## Slide 29: Single Optimization
vs
min for

## Slide 30
* variance-efficiency =

## Slide 32: Single Optimization
vs
min for

## Slide 33: Alternating Optimization
min for
odd n-1
even n-1

## Slide 35
+
for a given
Regularized Optimization

## Slide 41: To-Do