## Slide 1: PhD Progress Meeting 2013
Mathieu Boudreau
November 25th 2013
Biomedical Engineering Dept.
McGill University
Committee:
Prof. Bruce Pike – Supervisor
Dr. Douglas Arnold - External member
Prof. Robert Funnell - Chair’s representative
Development of Multimodal Quantitative MRI Techniques to Assess Brain Tissue Microstructure in Multiple Sclerosis

## Slide 2: Overview
Introduction
Reminder of Hypotheses
Progress
  Publications/Abstracts
  Work on Aim 1
Upcoming Research Plan/ Timeline
  Aim 1: qMT compressed sensing
  Aim 1: Completion of ISMRM work
  Aim 2: Post-mortem MS qMT
  Aim 3: MS Patient whole-brain qMT
Notes: BRIEF OVERVIEW OF Report

## Slide 3: Introduction
Multiple Sclerosis: disabling neurological disease affecting 55,000-75,000 Canadians.
MRI: imaging modality uniquely sensitive to many aspects of MS pathology.
Quantitative Magnetization Transfer: MRI technique capable of quantifying changes in myelin density.
Most qMT research of MS concentrate on white matter pathology, partly due to time and resolution limitations.
We aim to develop a fast high-resolution qMT method for white and gray matter MS pathology in the whole-brain to investigate the spatial relationship between pathology in both tissues.
3
Notes: TRIGGER of MS is unknown
there is currently NO CURE

## Slide 4: Introduction
Multiple Sclerosis: disabling neurological disease affecting 55,000-75,000 Canadians.
MRI: imaging modality uniquely sensitive to many aspects of MS pathology.
Quantitative Magnetization Transfer: MRI technique capable of quantifying changes in myelin density.
Most qMT research of MS concentrate on white matter pathology, partly due to time and resolution limitations.
We aim to develop a fast high-resolution qMT method for white and gray matter MS pathology in the whole-brain to investigate the spatial relationship between pathology in both tissues.
3
Notes: CONVENTIONAL MRI – CLINICAL DIAGNOSIS

## Slide 5: Introduction
Multiple Sclerosis: disabling neurological disease affecting 55,000-75,000 Canadians.
MRI: imaging modality uniquely sensitive to many aspects of MS pathology.
Quantitative Magnetization Transfer: MRI technique capable of quantifying changes in myelin density.
Most qMT research of MS concentrate on white matter pathology, partly due to time and resolution limitations.
We aim to develop a fast high-resolution qMT method for white and gray matter MS pathology in the whole-brain to investigate the spatial relationship between pathology in both tissues.
3
Notes: SOME MT MEASURES CORRELATE WITH MYELIN DENSITY

## Slide 6: Introduction
Multiple Sclerosis: disabling neurological disease affecting 55,000-75,000 Canadians.
MRI: imaging modality uniquely sensitive to many aspects of MS pathology.
Quantitative Magnetization Transfer: MRI technique capable of quantifying changes in myelin density.
Most qMT research of MS concentrate on white matter pathology, partly due to time and resolution limitations.
We aim to develop a fast high-resolution qMT method for white and gray matter MS pathology in the whole-brain to investigate the spatial relationship between pathology in both tissues.
3
Notes: qMT FOCUS WM LESIONS. RES LIMIT
+ MS CONSIDERED A WM DISEASE

## Slide 7: Introduction
Multiple Sclerosis: disabling neurological disease affecting 55,000-75,000 Canadians.
MRI: imaging modality uniquely sensitive to many aspects of MS pathology.
Quantitative Magnetization Transfer: MRI technique capable of quantifying changes in myelin density.
Most qMT research of MS concentrate on white matter pathology, partly due to time and resolution limitations.
We aim to develop a fast high-resolution qMT method for white and gray matter MS pathology in the whole-brain to investigate the spatial relationship between pathology in both tissues.
3

## Slide 8: Hypotheses
Whole-brain qMT maps can be acquired with a resolution of 1 mm3 in a clinically acceptable time of < 30 minutes.
High-resolution qMT WM/GM focal and diffuse pathology in post-mortem healthy and MS brains will correlate with immunohistochemistry measurements of pathology.
Is cortical GM MS pathology spatially independent of connectivity with WM lesions?
4
Notes: 3 HYPOTHESES FOR THIS PROECT ARE THE FOLLOWING

## Slide 9: Hypotheses
Whole-brain qMT maps can be acquired with a resolution of 1 mm3 in a clinically acceptable time of < 30 minutes.
High-resolution qMT WM/GM focal and diffuse pathology in post-mortem healthy and MS brains will correlate with immunohistochemistry measurements of pathology.
Is cortical GM MS pathology spatially independent of connectivity with WM lesions?
4

## Slide 10: Hypotheses
Whole-brain qMT maps can be acquired with a resolution of 1 mm3 in a clinically acceptable time of < 30 minutes.
High-resolution qMT WM/GM focal and diffuse pathology in post-mortem healthy and MS brains will correlate with immunohistochemistry measurements of pathology.
Is cortical GM MS pathology spatially independent of connectivity with WM lesions?
4

## Slide 11: List of Publications/Abstracts
Submitted Manuscripts
Nikola Stikov, Mathieu Boudreau, Ives Levesque, Christine Tardif, Joëlle Barral, G. Bruce Pike, “On the Accuracy of T1 Mapping: Searching for Common Ground”, Submitted to: Magnetic Resonance in Medicine
Accepted Conference Abstracts
Mathieu Boudreau, Nikola Stikov, G. Bruce Pike, “T1 Mapping: Should We Agree To Disagree?”, Poster, International Society for Magnetic Resonance in Medicine Meeting 2013
Mathieu Boudreau, Nikola Stikov, G. Bruce Pike, “Effect of Different T1 Mapping Techniques on a Quantitative Magnetization Transfer MRI Biomarker for Myelin Density”, Poster, endMS Conference 2013
Submitted Conference Abstracts
Mathieu Boudreau, Christine Tardif, Nikola Stikov, G. Bruce Pike, “A Comparison of B1 Mapping Methods for T1 Mapping at 3T”, Submitted to: International Society for Magnetic Resonance in Medicine Meeting 2014
Mathieu Boudreau, Nikola Stikov, G. Bruce Pike, “A B1 Insensitive qMT Protocol”, Submitted to: International Society for Magnetic Resonance in Medicine Meeting 2014
Ye Gu, Nikola Stikov, Mathieu Boudreau, Yaaseen Atchia, Ives Levesque, John Sled, G. Bruce Pike, “qMTLab: An Open Source Software Package for Quantitative Analysis of Magnetization Transfer”, Submitted to: International Society for Magnetic Resonance in Medicine Meeting 2014
5

## Slide 12: Progress – Aim 1 Section 4.1: Quantitative Comparison of B1 Mapping Methods for White Matter T1 Mapping at 3T
6
Continuation of Dr. Tardifs 2011 ISMRM work – a comparison B1 methods on VFA T1 values, in phantoms.
Fits in Aim 1, whole brain qMT protocols will require rapid B1 mapping techniques such as Actual-Flip-Angle Imaging (AFI)
This work compared VFA T1 maps in healthy WM using 4 B1 methods: Reference DA, BS, AFI, and EPI-DA.
Tardif et al, ISMRM 2011

## Slide 13: Progress – Aim 1 Section 4.1: Quantitative Comparison of B1 Mapping Methods for White Matter T1 Mapping at 3T
6
Continuation of Dr. Tardifs 2011 ISMRM work – a comparison B1 methods on VFA T1 values, in phantoms.
Fits in Aim 1, whole brain qMT protocols will require rapid B1 mapping techniques such as Actual-Flip-Angle Imaging (AFI)
This work compared VFA T1 maps in healthy WM using 4 B1 methods: Reference DA, BS, AFI, and EPI-DA.
Tardif et al, ISMRM 2011

## Slide 14: Progress – Aim 1 Section 4.1: Quantitative Comparison of B1 Mapping Methods for White Matter T1 Mapping at 3T
6
Continuation of Dr. Tardifs 2011 ISMRM work – a comparison B1 methods on VFA T1 values, in phantoms.
Fits in Aim 1, whole brain qMT protocols will require rapid B1 mapping techniques such as Actual-Flip-Angle Imaging (AFI)
This work compared VFA T1 maps in healthy WM using 4 B1 methods: Reference DA, BS, AFI, and EPI-DA.
Tardif et al, ISMRM 2011

## Slide 15: Progress – Aim 1 Section 4.1: Quantitative Comparison of B1 Mapping Methods for White Matter T1 Mapping at 3T
7
All B1 methods provided comparable B1 and VFA T1 maps.
EPI-DA (5 s/slice), the fastest method, had no observable distortion.
Fig. 2 - Normalized pooled histograms of single slice WM T1 values for 6 healthy subjects.
Figure 1 – B1 and VFA T1 map comparison.

## Slide 16: Progress – Aim 1 Section 4.2: Effect of Different T1 Mapping Techniques on a Quantitative Magnetization Transfer MRI Biomarker for Myelin Density
8
Last year: Simulated the effect of erroneous T1 measurements on qMT.
To shorten the acquisition time of whole brain qMT, the conventional LL T1 measurements must be replaced by a rapid T1 technique.
Three commonly used T1 techniques (IR, LL, VFA) have been recently shown to disagree significantly in vivo.
This study investigated the effects of different T1 techniques on qMT parameters in WM of healthy subjects.
Fig. 3 Effect on qMT fitted parameters as a result of measuring a T1 value different from the true tissue T1 value (dotted line).

## Slide 17: Progress – Aim 1 Section 4.2: Effect of Different T1 Mapping Techniques on a Quantitative Magnetization Transfer MRI Biomarker for Myelin Density
8
Last year: Simulated the effect of erroneous T1 measurements on qMT.
To shorten the acquisition time of whole brain qMT, the conventional LL T1 measurements must be replaced by a rapid T1 technique.
Three commonly used T1 techniques (IR, LL, VFA) have been recently shown to disagree significantly in vivo.
This study investigated the effects of different T1 techniques on qMT parameters in WM of healthy subjects.
Fig. 3 Effect on qMT fitted parameters as a result of measuring a T1 value different from the true tissue T1 value (dotted line).

## Slide 18: Progress – Aim 1 Section 4.2: Effect of Different T1 Mapping Techniques on a Quantitative Magnetization Transfer MRI Biomarker for Myelin Density
8
Last year: Simulated the effect of erroneous T1 measurements on qMT.
To shorten the acquisition time of whole brain qMT, the conventional LL T1 measurements must be replaced by a rapid T1 technique.
Three commonly used T1 techniques (IR, LL, VFA) have been recently shown to disagree significantly in vivo.
This study investigated the effects of different T1 techniques on qMT parameters in WM of healthy subjects.
Fig. 3 Effect on qMT fitted parameters as a result of measuring a T1 value different from the true tissue T1 value (dotted line).

## Slide 19: Progress – Aim 1 Section 4.2: Effect of Different T1 Mapping Techniques on a Quantitative Magnetization Transfer MRI Biomarker for Myelin Density
8
Last year: Simulated the effect of erroneous T1 measurements on qMT.
To shorten the acquisition time of whole brain qMT, the conventional LL T1 measurements must be replaced by a rapid T1 technique.
Three commonly used T1 techniques (IR, LL, VFA) have been recently shown to disagree significantly in vivo.
This study investigated the effects of different T1 techniques on qMT parameters in WM of healthy subjects.
Fig. 3 Effect on qMT fitted parameters as a result of measuring a T1 value different from the true tissue T1 value (dotted line).

## Slide 20: Progress – Aim 1 Section 4.2: Effect of Different T1 Mapping Techniques on a Quantitative Magnetization Transfer MRI Biomarker for Myelin Density
9
Six healthy subjects were scanned as part of the protocol of our ISMRM study.
The overestimation in VFA T1 values deviated F away from IR less than for LL.
Fig. 4 Normalized pooled histograms of single slice WM quantitative MT parameter values for 6 healthy subjects .

## Slide 21: Progress – Aim 1 Section 4.3: Insensitivity of B1 on our qMT Protocol
10
An unexpected result (Fig) was observed when comparing qMT maps with different B1 maps + VFA T1 maps.
Here, B1 is used twice before fitting the qMT parameters: to correct the flip angles for T1 mapping, and to scale the nominal MT saturation powers.
What is the limit of this insensitivity to B1 maps on qMT F?
WM
DA
AFI
Fig. 6 Scatter plot of qMT F values calculating using VFA T1, and DA B1 maps (horizontal axis) and AFI B1 maps (vertical).

## Slide 22: Progress – Aim 1 Section 4.3: Insensitivity of B1 on our qMT Protocol
10
An unexpected result (Fig) was observed when comparing qMT maps with different B1 maps + VFA T1 maps.
Here, B1 is used twice before fitting the qMT parameters: to correct the flip angles for T1 mapping, and to scale the nominal MT saturation powers.
What is the limit of this insensitivity to B1 maps on qMT F?
WM
DA
AFI
Fig. 6 Scatter plot of qMT F values calculating using VFA T1, and DA B1 maps (horizontal axis) and AFI B1 maps (vertical).

## Slide 23: Progress – Aim 1 Section 4.3: Insensitivity of B1 on our qMT Protocol
10
An unexpected result (Fig) was observed when comparing qMT maps with different B1 maps + VFA T1 maps.
Here, B1 is used twice before fitting the qMT parameters: to correct the flip angles for T1 mapping, and to scale the nominal MT saturation powers.
What is the limit of this insensitivity to B1 maps on qMT F?
WM
DA
AFI
Fig. 6 Scatter plot of qMT F values calculating using VFA T1, and DA B1 maps (horizontal axis) and AFI B1 maps (vertical).

## Slide 24: Progress – Aim 1 Section 4.3: Insensitivity of B1 on our qMT Protocol
11
Comparison between DA B1 and Flat (homogeneous ) B1 maps
Fig. 7 Comparison of qMT F maps fitted using DA and flat (B1 = 1) B1 maps and VFA T1 maps.
Fig. 8 Pooled (all subjects) whole brain Pearson correlation coefficients (a) and linear regression slopes (b) for qMT F values between the measured DA B1 maps and simulated flat B1 maps.
The exact origin of the erroneous B1, and subsequently VFA T1, nearly cancelling out in qMT F maps remains to be clarified.

## Slide 25: Progress – Aim 1 Section 4.3: Insensitivity of B1 on our qMT Protocol
11
Comparison between DA B1 and Flat (homogeneous ) B1 maps
The exact origin of the erroneous B1, and subsequently VFA T1, nearly cancelling out in qMT F maps remains to be clarified.
Fig. 7 Comparison of qMT F maps fitted using DA and flat (B1 = 1) B1 maps and VFA T1 maps.
Fig. 8 Pooled (all subjects) whole brain Pearson correlation coefficients (a) and linear regression slopes (b) for qMT F values between the measured DA B1 maps and simulated flat B1 maps.

## Slide 26: Progress – Aim 1 Section 4.4: qMT Compressed Sensing
Developed sparse k-space 2D GRE sequence (base sequence for our qMT sequences)
Single point qMT sequence, UI MT parameter control (MT saturation, off-resonance frequency).
Siemens raw data Matlab code
An open source 3D L1-SPIRIT multi-channel sparse acquisition image reconstruction software package was installed and tested .
12

## Slide 27: Progress – Aim 1 Section 4.4: qMT Compressed Sensing
Developed sparse k-space 2D GRE sequence (base sequence for our qMT sequences)
Single point qMT sequence, UI MT parameter control (MT saturation, off-resonance frequency).
Siemens raw data Matlab code
An open source 3D L1-SPIRIT multi-channel sparse acquisition image reconstruction software package was installed and tested .
12

## Slide 28: Progress – Aim 1 Section 4.4: qMT Compressed Sensing
Developed sparse k-space 2D GRE sequence (base sequence for our qMT sequences)
Single point qMT sequence, UI MT parameter control (MT saturation, off-resonance frequency).
Siemens raw data Matlab code
An open source 3D L1-SPIRIT multi-channel sparse acquisition image reconstruction software package was installed and tested .
12

## Slide 29: Progress – Aim 1 Section 4.4: qMT Compressed Sensing
Developed sparse k-space 2D GRE sequence (base sequence for our qMT sequences)
Single point qMT sequence, UI MT parameter control (MT saturation, off-resonance frequency).
Siemens raw data Matlab code
An open source 3D L1-SPIRIT multi-channel sparse acquisition image reconstruction software package was installed and tested .
12

## Slide 30: Upcoming Research Plan Sections 5.1 & 6.1: qMT Compressed Sensing December 2013 - May 2014
qMT point by point sensitivity to CS-reconstruction
  L1-Spirit+Wavelet reconstruction
  Using single slice, 2x2x5 mm3 qMT data (5 healthy subjects)
  Using whole brain, 2x2x2 mm3 qMT data (1 RRMS patient)
Evaluate feasibility of locally low rank sparsity reconstruction
  Try on-hand data first
  May need to acquire more data
    LLR sensitive to in-scan motion
Acquire small set of whole brain hi-res qMT
  Compare qMT-point optimized L1-Spirit with LLR
13

## Slide 31: Upcoming Research Plan Sections 5.1 & 6.1: qMT Compressed Sensing December 2013 - May 2014
qMT point by point sensitivity to CS-reconstruction
  L1-Spirit+Wavelet reconstruction
  Using single slice, 2x2x5 mm3 qMT data (5 healthy subjects)
  Using whole brain, 2x2x2 mm3 qMT data (1 RRMS patient)
Evaluate feasibility of locally low rank sparsity reconstruction
  Try on-hand data first
  May need to acquire more data
    LLR sensitive to in-scan motion
Acquire small set of whole brain hi-res qMT
  Compare qMT-point optimized L1-Spirit with LLR
13

## Slide 32: Upcoming Research Plan Sections 5.1 & 6.1: qMT Compressed Sensing December 2013 - May 2014
qMT point by point sensitivity to CS-reconstruction
  L1-Spirit+Wavelet reconstruction
  Using single slice, 2x2x5 mm3 qMT data (5 healthy subjects)
  Using whole brain, 2x2x2 mm3 qMT data (1 RRMS patient)
Evaluate feasibility of locally low rank sparsity reconstruction
  Try on-hand data first
  May need to acquire more data
    LLR sensitive to in-scan motion
Acquire small set of whole brain hi-res qMT
  Compare qMT-point optimized L1-Spirit with LLR
13

## Slide 33: Upcoming Research Plan Sections 5.2 & 6.1: Complete ISMRM work December 2013 - May 2014
Simulate qMT sensitivity to B1 (for T1 = VFA(B1), IR)
  Modify current qMT simulation code
  Tissue parameters
    Pure WM
    Pure GM
    WM/GM partial volume
    GM/CSF partial volume
Compare smoothed and blurred B1 maps for all methods
  Better agreement in overall T1 maps?
14

## Slide 34: Upcoming Research Plan Sections 5.3 & 6.2: Post-mortem MS qMT June 2014 - December 2014
Optimize qMT pulse sequence for reductions in post-mortem brains T1 values due to formaldehyde fixation.
Post-mortem brain hemispheres (1 healthy, 4 MS for different stages) to be scanned Summer/Fall 2014.
Statistical analysis of MRI scans and immunohistochemicaly stained coronal slices.
15

## Slide 35: Upcoming Research Plan Sections 5.3 & 6.2: Post-mortem MS qMT June 2014 - December 2014
Optimize qMT pulse sequence for reductions in post-mortem brains T1 values due to formaldehyde fixation.
Post-mortem brain hemispheres (1 healthy, 4 MS for different stages) to be scanned Summer/Fall 2014.
Statistical analysis of MRI scans and immunohistochemicaly stained coronal slices.
15

## Slide 36: Upcoming Research Plan Sections 5.3 & 6.2: Post-mortem MS qMT June 2014 - December 2014
Optimize qMT pulse sequence for reductions in post-mortem brains T1 values due to formaldehyde fixation.
Post-mortem brain hemispheres (1 healthy, 4 MS for different stages) to be scanned Summer/Fall 2014.
Statistical analysis of MRI scans and immunohistochemicaly stained coronal slices.
15

## Slide 37: Upcoming Research Plan Sections 5.4, 6.3 & 6.4: In vivo whole-brain MS qMT January 2015 - August 2015
3D qMT protocol on secondary progressive MS patients and age/sex matched healthy volunteers.
Investigate cortical GM qMT values in healthy GM and GM lesions.
Acquire high angular resolution MRI diffusion tractography maps.
qMT parameters in cortical GM connected to WM lesions will be investigated to determine if they exhibit statistically different values compared to contra-lateral regions free of WM lesions.
16

## Slide 38: Thesis Completion Timeline
17

## Slide 40: PhD Progress Meeting 2013
Mathieu Boudreau
November 25th 2013
Biomedical Engineering Dept.
McGill University
Committee:
Prof. Bruce Pike – Supervisor
Dr. Douglas Arnold - External member
Prof. Robert Funnell - Chair’s representative
Development of Multimodal Quantitative MRI Techniques to Assess Brain Tissue Microstructure in Multiple Sclerosis