## Slide 1: PhD Progress Meeting 2014
Mathieu Boudreau
December 18th 2014
Biomedical Engineering Dept.
McGill University
Committee:
Prof. Bruce Pike – Supervisor
Dr. Douglas Arnold - External member
Prof. Robert Funnell - Chair’s representative
Development of Multimodal Quantitative MRI Techniques to Assess Brain Tissue Microstructure in Multiple Sclerosis

## Slide 2: Overview
Reminder of Hypotheses
  Updated proposed manuscripts
List of Publications/Abstracts
Training & Collaborations
Progress
  Publications/Abstracts
  Manuscript 1 Progress
  Manuscript 2 Progress
  Manuscript 3 (Optional)
  Manuscript 4 Progress
Upcoming Research Plan
Timeline
Notes: BRIEF OVERVIEW OF Report

## Slide 3: Previous Hypotheses
Whole-brain qMT maps can be acquired with a resolution of 1 mm3 in a clinically acceptable time of < 30 minutes.
High-resolution qMT WM/GM focal and diffuse pathology in post-mortem healthy and MS brains will correlate with immunohistochemistry measurements of pathology.
Is cortical GM MS pathology spatially independent of connectivity with WM lesions?
Notes: 3 HYPOTHESES FOR THIS PROECT ARE THE FOLLOWING

## Slide 4: Previous Hypotheses
Whole-brain qMT maps can be acquired with a resolution of 1 mm3 in a clinically acceptable time of < 30 minutes.
  B1 Method Comparison for Whole-Brain T1 Mapping (ISMRM 2014)
  B1-sensitivity of qMT (ISMRM 2014, ISMRM 2015)
High-resolution qMT WM/GM focal and diffuse pathology in post-mortem healthy and MS brains will correlate with immunohistochemistry measurements of pathology.
Is cortical GM MS pathology spatially independent of connectivity with WM lesions?
Notes: 3 HYPOTHESES FOR THIS PROECT ARE THE FOLLOWING

## Slide 5: Previous Hypotheses
Whole-brain qMT maps can be acquired with a resolution of 1 mm3 in a clinically acceptable time of < 30 minutes.
  B1 Method Comparison for Whole-Brain T1 Mapping (ISMRM 2014)
  B1-sensitivity of qMT (ISMRM 2014, ISMRM 2015)
High-resolution qMT WM/GM focal and diffuse pathology in post-mortem healthy and MS brains will correlate with immunohistochemistry measurements of pathology.
Is cortical GM MS pathology spatially independent of connectivity with WM lesions?
Notes: 3 HYPOTHESES FOR THIS PROECT ARE THE FOLLOWING

## Slide 6: Revised Aims
Comparing quantitative transmit radiofrequency field (B1) mapping methods for whole-brain variable flip angle T1 maps
An analysis of the B1-sensitivity of qMT parameters
Quantitative MT acquisitions can be optimized for both white and grey matter sensitivity over the whole brain with a resolution of 1 mm3 in a clinically acceptable time of <30 minutes.
Notes: 3 HYPOTHESES FOR THIS PROECT ARE THE FOLLOWING

## Slide 7: List of Publications/Abstracts
Submitted Manuscripts
Nikola Stikov, Jennifer S.W. Campbell, Thomas Stroh, Stephen Frey, Jennifer Novek, Stephen Nuara, Ming-Kai Ho, Barry J. Bedell, Robert F. Dougherty, Ilana R. Leppert, Mathieu Boudreau, Sridar Narayanan, and G. Bruce Pike, “In vivo histology of the myelin g-ratio with magnetic resonance imaging”, Neuroimage, (Submitted on: December 5th 2014)
Published Manuscripts
Nikola Stikov, Mathieu Boudreau, Ives Levesque, Christine Tardif, Joëlle Barral, G. Bruce Pike, “On the Accuracy of T1 Mapping: Searching for Common Ground”, Magnetic Resonance in Medicine, DOI: 10.1002/mrm.25135 (2014)
Manuscripts in Progress
Mathieu Boudreau, Christine Tardif, Nikola Stikov, G. Bruce Pike, “A Comparison of B1 Mapping Methods for T1 Mapping at 3T”, Proposed submission to: Magnetic Resonance in Medicine, Format: Technical Note (2015)
Mathieu Boudreau, Nikola Stikov, Douglas L. Arnold, G. Bruce Pike, “B1-Sensitivity Analysis of qMT”, Proposed submission to: Magnetic Resonance in Medicine, Format: Full Paper (2015)
Proposed Manuscripts
Mathieu Boudreau, Nikola Stikov, Stephen Cauley, G. Bruce Pike, “Analytical Analysis of B1-Sensitivity of Quantitative Magnetization Imaging”, Proposed submission to: Medical Physics, Format: Technical Note (2015)
Mathieu Boudreau, Ives R. Levesque, David Rudko, Tao Zhang, Douglas L. Arnold, G. Bruce Pike, “Optimized Acceleration of Quantitative Magnetization Transfer Parameter Mapping Using Locally Low Rank Sparsity”, Proposed submission to: Magnetic Resonance in Medicine, Format: Full Paper (2015)

## Slide 8: List of Publications/Abstracts
Peer Reviewed Conference Abstracts
N. Stikov, J. Campbell, M. Boudreau, S. Narayanan, T. Stroh, S. Nuara, J. Novek, S. Frey, M.-K. Ho, B. Bedell, G. B. Pike, “In vivo histology of the myelin g-ratio”, Poster, OHBM Annual Meeting (2014)
Mathieu Boudreau, Nikola Stikov, G. Bruce Pike, “A B1 Insensitive qMT Protocol”, Poster, International Society for Magnetic Resonance in Medicine Meeting (2014)
Mathieu Boudreau, Christine Tardif, Nikola Stikov, G. Bruce Pike, “A Comparison of B1 Mapping Methods for T1 Mapping at 3T”, E-Poster, International Society for Magnetic Resonance in Medicine Meeting (2014)
Mathieu Boudreau, Nikola Stikov, G. Bruce Pike, “Effect of Different T1 Mapping Techniques on a Quantitative Magnetization Transfer MRI Biomarker for Myelin Density”, Poster, endMS Conference (2013)
Mathieu Boudreau, Nikola Stikov, G. Bruce Pike, “T1 Mapping: Should We Agree To Disagree?”, Poster, International Society for Magnetic Resonance in Medicine Meeting (2013)
Submitted Conference Abstracts
Mathieu Boudreau, Nikola Stikov, G. Bruce Pike, “B1-Sensitivity Analysis of qMT”, Submitted to: International Society for Magnetic Resonance in Medicine Meeting 2015
Ye Gu, Mathieu Boudreau, Ives R Levesque, Yaaseen Atchia, John Sled, Sridar Narayanan, Douglas L. Arnold, Bruce Pike, and Nikola Stikov, “Quantitative Magnetization Transfer Analysis: An Interactive Introduction with qMTLab”, Submitted to: International Society for Magnetic Resonance in Medicine Meeting 2015

## Slide 9: 2014 Training
2013 endMS conference (Saint-Sauveur)
  scholarship covering the complete cost of attending the conference.
  communication workshop by the Alan Alda Center for Communicating Science).
  Presented work
    1 traditional poster
2014 ISMRM meeting (Milan)
  ISMRM Trainee Educational Stipend
  Educational Weekend
  Presented work
    1 traditional poster
    1 electronic poster.
endMS Network workshops (Montreal)
  endMS Statistics Series.
Software Carpentry workshop (Montreal)
2014 MS Exchange Conference (Montreal).

## Slide 10: 2014 Collaborations
Dr. Nikola Stikov and Dr. Jennifer Campbell (MNI)
  g-ratio project – acquisition/analysis of qMT in MS patient and macaque monkey.
  co-authorship in a recently submitted manuscript (Appendix D).
Dr. Julien Cohen-Adad (Polytechnique Montreal) and Dr. Stikov
  Over several months, I was involved with planning, acquiring, and analyzing qMT data in pig and cat spinal cords on our human 3T MRI at the MNI, and the animal 7T scanner at the Montreal Heart Institute.
Dr. Jacqueline Chen (Lerner Research Institute, Cleveland, Ohio)
  Implementation of an AFI B1 mapping acquisition and analysis on their scanner.
Dr. Aviv Mezer (Stanford University)
  Exploring the feasibility of improved fitting the MT exchange rate kf by fixing F in the model using his macromolecular tissue volume biomarker for myelin.
Dr. David Rudko and Dr. Robert Brown (MNI)
  Assistance with acquiring and analyzing qMT data using our qMT software.
Melany Ann McLean (University of Calgary, Dr. Pike’s lab)
  Assistance with qMT data analysis development for a small animal project.

## Slide 11: Progress – Manuscript 1 Section 4.1: Quantitative Comparison of B1 Mapping Methods for White Matter T1 Mapping at 3T (90% complete)
Background
  Several highly cited novel B1 methods have recently been developed for whole-brain imaging
  We intend to show that k-space accelerated (in our case EPI) DA is a valid alternative to these methods, and that all methods produce T1 maps in good agreement with each other
  An important advantage to this method is that it uses stock scanner sequences, no pulse sequence programming required.
Aim: Compare VFA T1 maps in WM produced with four B1 methods (ISMRM2014):
  Conventional double angle (Ref. DA),
  Bloch-Siegert (BS)
  Actual Flip-Angle Imaging (AFI)
  DA spin-echo EPI (EPI-DA).
Proposed manuscript format: Technical report, MRM

## Slide 12
Tissue classification maps (2x2x5 mm3, black = 0%, grey = 100%) of a typical healthy subject predicted from INSECT using MPRAGE T1w data (1x1x1 mm3), and resampled using a majority voting analysis.
Section 4.1: Quantitative Comparison of B1 Mapping Methods for White Matter T1 Mapping at 3T (90% complete)

## Slide 13
Figure 1. Normalized pooled histograms of single slice WM T1 values for 6 healthy subjects (bin width = 10 ms).
Section 4.1: Quantitative Comparison of B1 Mapping Methods for White Matter T1 Mapping at 3T (90% complete)

## Slide 15
 | Ref. DA | BS | AFI | EPI-DA
Pearson ρ | ----------- | 0.97 | 0.97 | 0.99
Fit slope | ----------- | 0.98 | 1.00 | 0.97
Figure 5: Table listing the linear regression analysis of the pooled WM T1 values (6 subjects) for each B1 method relative to the reference DA B1 method.
Section 4.1: Quantitative Comparison of B1 Mapping Methods for White Matter T1 Mapping at 3T (90% complete)

## Slide 16
Figure 2. (Top) Raw B1 acquisition images for each method. (Bottom) (a) Single slice B1 maps from a representative subject. (b) WM VFA T1 maps using flip angles corrected with each B1 map.
Section 4.1: Quantitative Comparison of B1 Mapping Methods for White Matter T1 Mapping at 3T (90% complete)

## Slide 17
Figure 3. Sagittal (left hemisphere) B1 maps for a single subject using the reference and EPI double angle methods.
Section 4.1: Quantitative Comparison of B1 Mapping Methods for White Matter T1 Mapping at 3T (90% complete)

## Slide 18
Figure 4. Comparison between raw B1 maps and filtered maps using: (a) Gaussian blurring (b) spline smoothing.
Section 4.1: Quantitative Comparison of B1 Mapping Methods for White Matter T1 Mapping at 3T (90% complete)

## Slide 19: Progress – Manuscript 2 Section 4.2: B1-Sensitivity Analysis of qMT (80% complete)
qMT imaging – requires additional qMRI measurements (B0, B1,T1)
These are typically independent of each other
  but certain T1 mapping techniques also require B1 maps (e.g. variable flip angle – VFA).
For VFA T1, B1 is used twice before fitting the qMT parameters
  to correct the flip angles for T1 mapping
  to scale the nominal MT saturation powers and excitation FA.
Inaccuracies in B1 would propagate to the fitting of the qMT parameters through two pathways
  errors induced in T1
  errors in MT saturation powers and excitation FA
This work demonstrated that for the Sled and Pike SPGR qMT model, the pool-size ratio F much less sensitive B1 inaccuracies when using VFA for T1 mapping.
Proposed manuscript format: Full Paper, MRM

## Slide 20: Progress – Manuscript 2 Section 4.2: B1-Sensitivity Analysis of qMT (80% complete)
Separated into 5 parts
Noiseless simulation of single tissue qMT for B1/T1 inaccuracies (ISMRM 2015)
B1-sensitivity of qMT parameters in-vivo (ISMRM 2014)
Comparison using 3 B1 mapping methods
B1-sensitivity of qMT parameters in pathology: RRMS patient
Insights on the origin of the qMT F B1-insensitivity

## Slide 21
Figure 6: Percent error in fitted qMT F values in the presence of a wide range of B1 and T1 errors (B1,true = 1 n.u., T1,true = 0.9 s). The superimposed lines plot the T1 distribution for a B1-independent T1 mapping method (IR, solid line) and VFA (dashed line).
Section 4.2 – Part 1: Noiseless simulation of single tissue qMT for B1/T1 inaccuracies

## Slide 22
Figure 7: Percent error in fitted qMT parameters for a range of B1 errors (a – pool size ratio (F), b – magnetization exchange rate (kf), c – free pool T2 (T2f), d – restricted pool T2 (T2r)). Fits using a B1-independent T1 measure (IR) are shown in red, and those using VFA T1 mapping are shown in blue. See solid and dashed lines in Fig. 2 for B1 dependence of IR and VFA T1.
Section 4.2 – Part 1: Noiseless simulation of single tissue qMT for B1/T1 inaccuracies

## Slide 23
Figure 8: A single subject comparison of qMT F maps fitted using DA and flat (B1 = 1) B1 maps using (a) VFA T1 maps corrected using the corresponding B1 map and (b) IR T1 maps independent of B1.
Section 4.2 – Part 2: B1-sensitivity of qMT parameters in-vivo

## Slide 24
Figure 9: a – Histogram of B1 error in the nominal B1 (Flat B1 = 1) assumption relative to the DA B1 map in a single subject. b – Histogram of fitted qMT F error % between nominal and DA B1 map, when using IR (red) or VFA (blue) T1 mapping. c – Histogram of fitted qMT kf error % between nominal and DA B1 map, when using IR (red) or VFA (blue) T1 mapping.
Section 4.2 – Part 2: B1-sensitivity of qMT parameters in-vivo

## Slide 25
(a)
(b)
Figure 10: Pooled (all subjects) whole brain Pearson correlation coefficients (a) and linear regression slopes (b) for qMT F values between the measured DA B1 maps and simulated flat B1 maps.
Section 4.2 – Part 2: B1-sensitivity of qMT parameters in-vivo

## Slide 26
Figure 11: Pooled (all subjects) whole brain Pearson correlation coefficients and linear regression slopes for qMT F values between the measured DA B1 maps and simulated flat B1 maps.
Section 4.2 – Part 2: B1-sensitivity of qMT parameters in-vivo

## Slide 27
Figure 12: Single-subject WM pool-size ratio (a, b) and exchange coefficient (c, d) distributions for 3 B1 mapping methods, using IR T1 mapping (a, c) and VFA T1 mapping (b, d).
Section 4.2 – Part 3: Comparison using 3 B1 mapping methods

## Slide 28
Section 4.2 – Part 4: B1-sensitivity of qMT parameters in pathology: RRMS patient
qMT F Maps

## Slide 29
Figure 13: Sensitivity analysis of the MT signal for changes in tissue or fitting variables: a – 5 % increase in B1 relative to the true B1, T1 independent of B1 b – 5 % increase in B1 relative to the true B1, T1 dependent of B1 (VFA) c – 10% increase in the pool-size ratio F d – 10% increase in the MT exchange coefficient kf.
Section 4.2 – Part 5: Insights on the origin of the qMT F B1-insensitivity

## Slide 30: Progress – Manuscript 3 (optional) Section 4.3: Analytical qMT Sensitivity Analysis
Approximated from Taylor expansion
Defining the sensitivity parameter
Equation for complete measurement set (N = # qMT points)
Solving for the parameter changes column vector (small phi)
ψ
Ψ
S
Proposed manuscript format: Technical Note or Full Paper, Medical Physics

## Slide 31: Progress – Manuscript 4 Section 4.4: qMT Compressed Sensing (20% complete)
Developed sparse k-space 2D GRE sequence (base sequence for our qMT sequences)
Single point qMT sequence, UI MT parameter control (MT saturation, off-resonance frequency).
Siemens raw data Matlab code
An open source 3D L1-SPIRIT multi-channel sparse acquisition image reconstruction software package was tested on preliminary data.
Raw k-space data acquired
  5 healthy subjects
  Two sets of qMT protocols: UK (uniform) and Optimized.
Proposed manuscript format: Full Paper, MRM

## Slide 32: Upcoming Research Plan Completing Manuscripts 1 & 2 January 2015- March 2015
Finish writing manuscript #1
Analyze MS data for manuscript #2
Write manuscript #2

## Slide 33: Upcoming Research Plan Sections 5.1 & 6.1: qMT Compressed Sensing March 2015 - September 2015
qMT point by point sensitivity to CS-reconstruction
  L1-Spirit+Wavelet reconstruction
  Using single slice, 2x2x5 mm3 qMT data (5 healthy subjects)
Compare with locally low rank sparsity reconstruction
  Try on-hand data first
  May need to acquire more data
    LLR sensitive to in-scan motion
Acquire small set of whole brain hi-res qMT
  Compare qMT-point optimized L1-Spirit with LLR

## Slide 34: Upcoming Research Plan Sections 5.1 & 6.1: qMT Compressed Sensing March 2015 - September 2015
Optimize qMT sequence for 3D measurement
  Aim for 15 ms TR
Pulse Sequence Mods. | Hard Limits | List of Consequences to Seq. Mods.
Shorten MT spoiler gradient | Max . gradient strength | /w MT pulse shortening, may have induced diffusion weighted spin echo at readout (shorter diff time). Risks affecting highest MT/smallest offres freq.
 | Slew rate | Eddie currents
Shorten MT pulse | Peak B1 | Strong enough MT signal saturation from high MT FA may not be achievable
 | SAR | 
Increase readout bandwith | Max . gradient strength | SNR decrease
 | Slew rate | 
Shorten TR | TE ( & bandwidth) | SAR increase
 | MT Pulse Duration | SNR decrease
 | MT Spoiler Duration | 
Shorten TE | Readout bandwidth | Small SNR increase, but overshadowed by bandwidth change

## Slide 35: Thesis Completion Timeline

## Slide 37: PhD Progress Meeting 2014
Mathieu Boudreau
December 18th 2014
Biomedical Engineering Dept.
McGill University
Committee:
Prof. Bruce Pike – Supervisor
Dr. Douglas Arnold - External member
Prof. Robert Funnell - Chair’s representative
Development of Multimodal Quantitative MRI Techniques to Assess Brain Tissue Microstructure in Multiple Sclerosis