## Slide 1
--
Effect of Different T1 Mapping Techniques on a Quantitative Magnetization Transfer MRI Biomarker for Myelin Density
Mathieu Boudreau1, Nikola Stikov1, G. Bruce Pike2
1McConnell Brain Imaging Center, Montreal Neurological Institute, McGill University, Montreal, Quebec, 2Hotchkiss Brain Institute, Faculty of Medicine, University of Calgary, Calgary, Alberta
This work explored the effect of three different T1 mapping techniques on the qMT parameter F, a biomarker for myelin density, in white matter of healthy subjects.
VFA underestimated WM F by 5 % relative to IR, and LL overestimated F by 27 %.
MS Researchers using qMT should report typical IR gold standard healthy WM T1 values for their site/scanner when other methods such as VFA are used.
The quantitative MT (qMT) parameter F (macromolecular pool size ratio) correlates strongly with histological measures of myelin in post-mortem MS brains1.
T1 maps, required for qMT, have recently been observed to vary in white matter (WM) between three commonly used methods at 3T2.
Literature WM T1 values also vary across scanners and sites.
This study investigated the effect of three different T1 mapping techniques on the qMT parameter F, a biomarker for myelin density, in white matter of healthy subjects.
References: [1] K. Schmierer et al., J. Magn. Res. Imag. 26:41-51 (2007) [2] N. Stikov et al., ‘Validation of T1 Mapping Techniques: Are Phantom Studies Sufficient’ Proc. of ISMRM (2012) [3] L. Collins et al. IPMI 1999, LNCS, Vol. 1613, Springer, Heidelberg 210-223 (1999) [4] Levesque I. et al, Magn. Res. in Med 66:635-643 (2011) [5] Sled J. and Pike G. B., MRM 46:923-931 (2001)
Introduction
Siemens 3T Tim Trio MRI system, 32-channel head coil
6 healthy adult volunteers
Single slice, AC-PC orientation, slightly above the corpus callosum (2x2x5 mm3)
White matter tissue masks: 1x1x1 mm3 MP-RAGE classified using INSECT3 (WM, GM, CSF). WM masks were resampled to match the qMT slice using a majority voting algorithm.
Pulse Sequences
B0  Two-point GRE phase-difference method
B1  Double angle method
T1  Three methods compared: Inversion recovery (IR, gold standard), Look-Locker (LL), and Variable Flip Angle (VFA)
qMT  Spoiled GRE optimal 10-point protocol4, Gaussian-Hanning MT pulses, Sled and Pike qMT model5
Methods
Contact: mathieu.boudreau2@mail.mcgill.ca
Acknowledgments: This work was funded by the Natural Sciences and Engineering Research Council’s Doctoral Alexander Graham Bell Canada Graduate Scholarship (M.B.), and grant funding was provided by the Canadian Institutes of Health Research.
Figure 2 shows a single-subject comparison between WM T1 maps produced using three T1 mapping methods (IR, LL, VFA), and the qMT F maps produced using each T1 map.
Results
Overestimations in WM T1 measured with VFA (relative to IR) resulted in a 5 % reduction in mean qMT F values (Table 1).
The 6-subject pooled WM VFA T1 distribution is broader than IR (Fig. 3a), the VFA F distribution was 25% narrower (Fig. 3b).
Unlike LL and IR, VFA requires a B1 map, thus inaccuracies in B1 propagate through two pathways into F when using VFA.
These results suggest that VFA may be a better alternative compared to LL for fast qMT mapping, and that gold standard IR T1 values should be reported when using alternative T1 methods.
Discussion
Figure 3a shows the pooled 6-subject WM T1 histograms for IR (black), LL (blue) and VFA (red). Figure 3b shows the pooled WM F histograms depending on the T1 method used. The T1 values for each method agree with previously reported values2. The differences in F between methods were modest in comparison to those observed in T1.
Results
Table 1 shows the pooled mean, pooled standard deviation, and intersubject standard deviation of F. Relative to IR, LL overestimated F by 27%, and VFA underestimated it by 5%. The pooled VFA histogram was 25% narrower than IR, which which cannot be explained by intersubject variations in F.
Results
qMT
B0
T1
B1
VFA
IR
LL
OR
OR
Figure 1. Quantitative MRI protocol processing hierarchy.
Figure 3. WM T1 (IR, LL, VFA) and qMT F pooled histograms for 6 subjects.
T1 | Pooled F Mean | Pooled F SD | Intersubject F SD
IR | 0.182 | ± 0.036 | ± 0.005
LL | 0.232 | ± 0.041 | ± 0.008
VFA | 0.172 | ± 0.027 | ± 0.004
Table 1. Statistics of WM F values for 6 subjects using 3 T1 methods.
Pooled F SD is the standard deviation of the pooled F values (Figure 2b). Intersubject F SD is the standard deviation of the mean F between subjects.
T1
(s)
qMT F
(n.u.)
IR
9m16s / slice
LL
2m20s / slice
VFA
3s / slice
Figure 2. WM T1 maps T1 (IR, LL, VFA) and qMT F maps of a healthy adult subject.
1.4
1.2
1.0
0.8
0.6
0.4
0.3
0.2
0.1
0.0
Summary
b
a