## Slide 1
--
Mathieu Boudreau1, Nikola Stikov1, G. Bruce Pike2
1McConnell Brain Imaging Center, Montreal Neurological Institute, McGill University, Montreal, Quebec, 2Hotchkiss Brain Institute and Department of Radiology, University of Calgary, Calgary, Alberta, Canada
This work demonstrated that qMT F maps fitted using VFA T1 can be insensitive to B1 inaccuracies.
A strong correlation (ρ = 0.99) between qMT F parameter values fitted using measured and nominal B1 maps was observed when using VFA T1.
More work in simulating the effects of B1 and VFA T1 inaccuracies on qMT parameter estimation is needed to have a clearer understanding of the limitations of this observation.
Quantitative magnetization transfer (qMT) imaging requires B0 and B1 measurements to correct for instrumental biases, and a T1 measurement to constrain parameters in the fitting model.
If using Variable Flip Angle (VFA) T1 mapping1, B1 is used twice before fitting the qMT parameters: to correct the flip angles for T1 mapping, and to scale the nominal MT saturation powers.
Inaccuracies in B1 would propagate to the fitting of the qMT parameters through two pathways – through errors induced in T1, and errors in MT saturation powers.
This work demonstrates that for the Sled and Pike qMT model2, certain qMT parameters are insensitive to a large range of B1 inaccuracies when using VFA for T1 mapping.
References: [1] Deoni S. et al, MRM 49:515-526 (2003) [2] Sled J. and Pike G. B., MRM 46:923-931 (2001) [3] Yarnykh V., MRM 63:1610-26 (2010) [4] Barral J. et al, MRM 64:1057-1067 (2010) [5] http://www-mrsrl.stanford.edu/∼jbarral/t1map.html (Accessed: October 2012) [6] Levesque I. et al, MRM 66:635-643 (2011) [7] Schmierer K. et al, JMRI 26:41-51 (2007) [8] Yarnykh V., MRM 68:166-178 (2012)
Introduction
Siemens 3T Tim Trio MRI system, 32-channel head coil
3 healthy adult volunteers
Single slice, AC-PC orientation, slightly above the corpus callosum (2x2x5 mm3)
Pulse Sequences
B0  Two-point GRE phase-difference method
B1  Double angle method (DAM) (α = 60°/120° )
T1  Variable Flip Angle3 (TR =15 ms, α = 3°/20°)
 Inversion recovery4,5 (TI = 30, 530, 1030, 1530 ms )
qMT  Spoiled GRE optimal 10-point protocol6, Gaussian-Hanning MT pulses, Sled and Pike qMT model2
Simulated B1 Errors
B1  Flat B1 maps = 0.5, 0.75, 0.9, 1, 1.1, 1.25, 1.5, 2 n.u.
Methods
Contact: mathieu.boudreau2@mail.mcgill.ca
Acknowledgments: This work was funded by the Natural Sciences and Engineering Research Council’s Doctoral Alexander Graham Bell Canada Graduate Scholarship (M.B.), and grant funding was provided by the Canadian Institutes of Health Research.
Results – Measured B1 vs. Nominal FA
VFA-based T1 maps renders qMT F and T2,f insensitive to B1 errors.
Processing qMT F maps using VFA T1 and a flat B1 map results in nearly identical qMT F maps to using measured DA B1 maps, (Fig. 2), except where CSF partial volume effects are suspected.
Severe overestimation of B1 is better tolerated than severe underestimation for the qMT parameter F (Fig. 3).
The exact origin of the erroneous B1 and VFA T1 nearly cancelling out in qMT F maps remains to be clarified.
A possible explanation might be that errors in B1 propagate to F via counterbalancing effects on T1 estimation and MT saturation power.
Discussion
Figure 3 shows the pooled whole brain Pearson correlation coefficients (a) and linear regression slopes (b) for qMT F parameter values between the measured DA B1 maps and simulated flat B1 maps, for VFA (blue) and IR (red) T1 maps.
High correlation (a) and linear regression slope values near 1 (b) for qMT F values are observed using VFA T1 maps for a large range of flat B1 maps (0.75 - 2 n.u.). qMT F maps fitted using IR T1 are sensitive B1 errors, as expected.
Results – VFA vs. IR
Results – qMT Parameters
Figure 1. Quantitative MRI protocol processing hierarchy.
Figure 3. Linear regression analysis of the voxelwise qMT F parameter, comparing measured DA B1 and a range of flat B1 (VFA T1, blue; IR T1, red).
Table 1. Voxelwise linear regression analysis of all fitted qMT parameters, using each T1 method (VFA - left, IR-right), and a comparison of the measured (DA) and nominal FA (B1 flat = 1) maps.
Summary
 | vs. |  | vs. | 
qMT | Pearson ρ | Slope | Pearson ρ | Slope
F | 0.99 | 0.98 | 0.81 | 0.81
kf | 0.32 | 0.31 | 0.52 | 0.57
R1f | 0.81 | 0.98 | 0.78 | 0.71
T2f | 0.99 | 0.95 | 0.93 | 1.02
T2r | 0.92 | 0.90 | 0.87 | 0.91
Figure 2. Comparison of VFA T1 and qMT F maps using measured (DA) and nominal (B1 flat = 1) B1 maps.
qMT
B0
T1
B1
VFA
IR
OR
DAM
Flat B1
OR
Flat B1
qMT
IR
DAM
qMT
IR
Flat B1
qMT
VFA
DAM
qMT
VFA
A B1-Insensitive qMT Protocol
a
b
Flat B1 amplitude (n.u.)
Flat B1 amplitude (n.u.)
Linear Regression Slope
Pearson Correlation Coefficient for F