## Slide 1
--
Mathieu Boudreau1, Nikola Stikov2, G. Bruce Pike3
1McConnell Brain Imaging Center, Montreal Neurological Institute, McGill University, Montreal, Quebec, 2Department of Electrical Engineering, Ecole Polytechnique de Montreal, Montreal, Quebec, Canada,3Hotchkiss Brain Institute, Department of Radiology, Faculty of Medicine, University of Calgary, Calgary, Alberta, Canada
This work demonstrated that pulsed qMT pool-size ratio F maps fitted using VFA T1 are nearly insensitive to B1 inaccuracies.
Under certain circumstances, B1 mapping could be omitted altogether without substantial bias to F values.
Pulsed qMT using B1-independent measures of T1 (e.g. IR) may be better suited for MT exchange rate (kf) mapping.
Further sensitivity analysis of the qMT equations for different measurement protocols could be used to determine optimal qMT protocols for reduced B1- sensitivity.
References: [1] Stikov, n. et al, MRM, doi: 10.1002/mrm.25135 (2014) [2] Boudreau, M. et al, Proc. of ISMRM, #3207 (2014) [3] Boudreau, M. et al, Proc. of ISMRM, #3167 (2014) [4] Sled J. and Pike G. B., JMR, 145:24-36 (2000) [5] Sled J. and Pike G. B., MRM, 46:923-931 (2001) [6] Stikov, N. et al, MRM, 66:725-734 (2011) [7] Harrison, N. et al, Biological Psychiatry, DOI: 10.1016/j.biopsych.2014.09.023 (2014)
Introduction
Pulsed MT SPGR signals were simulated in MATLAB (MATLAB2011a, The Mathworks Inc.) using the Sled and Pike approximations4.
Healthy WM qMT Tissue Parameters
F = 0.122
kf = 3.97 s-1
R1f, R1r = 1.11, 1.0 s-1
T2f, T2r = 27.2 ms, 10.96 μs
qMT Protocol (SPGR)
TR = 25 ms
αexcitation = 7°
Gaussian-Hanning MT pulses
  Pulse duration =10.2 ms
  αMT = 142° and 426°
  Off-resonance frequencies (for each αMT) = 423.9 Hz, 1,087.5 Hz, 2,731.6 Hz, 6,861.6 Hz, and 17,235.4 Hz.
Data Fitting
The qMT signal was subsequently fitted5 for 10,000 B1 and T1 value combinations.
  T1 varied independently of B1 for this step (without any assumptions on the measurement method.).
  100 B1 values between 0.5 to 2 (B1,true = 1).
  100 T1 value between 0.1 s to 4 s (T1,true = 0.9 s).
qMT was also fitted using T1 from simulated VFA signals1:
  TR =25 ms, α = 3° and 20°, T1 = T1,true.
  T1 values were fitted from the VFA data using each B1 error value.
Methods
Contact: mathieu.boudreau2@mail.mcgill.ca
Acknowledgments: This work was funded by the Natural Sciences and Engineering Research Council’s Doctoral Alexander Graham Bell Canada Graduate Scholarship (M.B.), and grant funding was provided by the Canadian Institutes of Health Research.
Results – B1 vs. T1
Discussion
Results – VFA vs. IR
Results
Figure 2. Percent error in fitted qMT parameters for a range of B1 errors (a – pool size ratio (F), b – magnetization exchange rate (kf), c – free pool T2 (T2f), d – restricted pool T2 (T2r)). See solid and dashed lines in Fig. 1 for the B1-dependence of VFA (solid) and IR (dashed) T1.
The superimposed lines in Fig. 1 show the range of errors in the fitted pool-size ratio F using a B1-independent T1 method (e.g. IR) (solid line), and from VFA T1 mapping (dashed line).
Figure 2 shows the errors in fitted qMT parameters (F, kf, T2f, T2r) using B1-independent (IR) and VFA-measured T1 for a range of B1 inaccuracies that may be observed in vivo.
Errors in F induced by B1 errors were greatly reduced by using VFA T1 mapping (Fig. 2a - blue).
A substantial increase in errors of kf occurs for VFA relative to IR (Fig. 2b - blue), while T2r remains insensitive to B1 inaccuracies for both cases.
Summary
Figure 1. Percent error in fitted qMT F values in the presence of a wide range of B1 and T1 errors (B1,true = 1 n.u., T1,true = 0.9 s).
B1-Sensitivity Analysis of qMT
B1 mapping is an important measurement used to correct the excitation flip angle and MT saturation powers in pulsed quantitative magnetization transfer (qMT) imaging.
Additional measurements necessary for qMT (e.g. T1 mapping) may also require B1 maps. For example, variable flip angle (VFA) T1 mapping requires B1 maps, while inversion recovery (IR) typically does not1.
Local (e.g. artifacts) or global (e.g. systemic biases) inaccuracies in B1 mapping2 will propagate to the fitted qMT parameters differently, depending on the T1 method.
We present a simulation-based analysis of the B1 sensitivity of pulsed qMT, investigating the propagation of the B1 error to the qMT parameters using different T1 mapping methods (VFA vs. IR).
We demonstrates the pool-size ratio F is robust against B1 inaccuracies when VFA T1 mapping is used, but this comes at the cost of an increase in error in the exchange rate kf.
The qMT pool-size ratio F was shown to be nearly B1-error insensitive when using VFA T1 mapping (Fig. 2a - blue).
Using a B1-independent T1 measure, such as IR, produces large qMT F errors (>100% to -45% for B1 errors between ±30%, Fig. 2a – red). VFA T1 mapping kept qMT F errors within a moderate range (7% to -3%, Fig. 2a - blue).
These results suggest that, when investigating the pool-size ratio (a biomarker for white matter myelin density), VFA T1 mapping should be used in the pulsed qMT protocol to reduce the effects of B1 inaccuracies.
For applications of qMT where kf is the biomarker of interest (e.g. cartilage imaging6, systemic inflammation7), our results suggest that a B1-independent measure of T1 may be preferable instead of the VFA method (Fig. 2b – red).